USER’S MANUAL

MOBILE DUST EXTRACTOR

Model: ME 1300, ME 2800

CONTENT

1.	Safety	2

2.	Design of the mobile dust extractor	3

3.	Product Description	4

4.	Technical Data	5

5.	Intended Use	6

6.	WARNING	7

7.	Maintenance and Service	8

8.	Instructions for Maintenance	9

8.1.	Replacement of the Dust Bag	9

8.2.	Replacement of the Polyester Filter	10

8.3.	Replacement of the HEPA Filter(s)	11

8.4.	Manual Cleaning of the Polyester Filter (Back flush)	12

9.	Trouble-shooting	13

EC DECLARATION OF CONFORMITY	14

# Safety

Safety precautions with a safety alert symbol indicate a danger of injuries. Be sure to follow these safety precautions to protect against injuries or death!

Safety precautions without a safety alert symbol indicate a danger of damage.

IMPORTANT!

The following documents should be read through and understood by all involved staff before installation and start up as well as during use and at maintenance and service:

- This user’s manual

These instructions must be followed closely and kept at the place where the machine is used.

Installation and utilisation are only to be done by trained and authorised staff.

All instructions in this manual must be followed closely for the warranty to be valid.

# Design of the mobile dust extractor

Figure 1 Complete mobile dust extraction unit (ME 2800)

- Top cover of the cyclone

- Cyclone (filter housing) with filter

- Top of the HEPA filter housing

- Dust bag

- Lever for manual filter cleaning

- Strap to secure the dust bag

# Product Description

| Product designation | Mobile vacuum cleaner |
| --- | --- |
| Model | ME 1300, ME 2800 |
| Description | Mobile vacuum cleaner consisting of electrical motor, separator with one polyester filter and one or two HEPA filters according to the model. The mobile vacuum cleaner is principally made of iron and painted with powder coating. |

| Environment | When designing the mobile vacuum cleaner, the choice of material and production method has been very important. The mobile vacuum cleaner is recyclable to 98 %. Exceptions are some electrical components. No solvents are used during the coating, neither for cleaning nor coat mixing. |
| --- | --- |

| Material |  |
| --- | --- |
| Stand | Iron, quality SIS 1312 |
| Cyclone | Iron, quality SIS 1312 |
| Filter | End plates of metal or plastic. Filter material of cellulose or polyester |
| Motor | Aluminium, iron and copper |
| Plastic details | Polyethylene and polypropylene |
| Paint | Polyester powder, TGIC-free |
| Sealings | Natural rubber |

| Manufacturer | Centraction AB Industrivägen 7 SE-433 61 Sävedalen Sweden Tel: +46 (0)31 26 75 44 Fax: +46 (0)31 26 18 44 e-mail: info@centraction.com www.centraction.com |
| --- | --- |

# Technical Data

|  | ME-1300 | ME-2800 |
| --- | --- | --- |
| Size (LxWxH) | 48x70x105 cm | 56x80x112 cm |
| Weight (approx.) | 29 kg | 42 kg |
| Voltage | 230 V | 230 V |
| Current | 8 A | 16 A |
| Power consumption | 1,3 kW | 2,8 kW |
| Air volume | 230 m³/h | 420 m³/h |
| Vacuum | 265 mbar | 265 mbar |
| Dust bag | 15 l | 35 l |
| Sound level | 65 dB | 65 dB |
| Filter size | 1,4 m² | 3,0 m² |
| HEPA filter H13 | 1x0,5 m² | 2x0,5 m² |
| Filtration | 98,89% DOP | 98,89% DOP |
| Hose Ø | 50 mm | 50 mm |
| Filter cleaning | Semi-automatic | Semi-automatic |

# Intended Use

The mobile vacuum cleaners are intended for general cleaning both for commercial and industrial use.

The mobile vacuum cleaner in standard version is not intended for the suction of water or wet, explosive or inflammable material.

# WARNING

- Before any kind of maintenance or service is carried out, the power supply must be removed from the wall socket. This does not apply for the manual cleaning of the filter.

- The mobile vacuum cleaner is not to be used for vacuuming wet or damp material. If water or any wet or damp material should enter the mobile vacuum cleaner it must be stopped immediately and dried before it can be taken into use again.

- Under no circumstances must the mobile vacuum cleaner be used for suction of burning, glowing, explosive or inflammable fluids or material.

- If the filter shows any damages it must inevitably be replaced before the vacuum cleaner is taken into use to avoid damages on the vacuum pump.

- Always treat used filters and used dust bags carefully since they might contain hazardous dust. Put the used filter in a large plastic bag and seal it carefully. Always seal used dust bags too.

- The mobile vacuum cleaner must never be used without filter or dust bag.

- All service, repair, and trouble-shooting of the mobile vacuum cleaner is only to be done by authorised staff.

- Some dust may be harmful to the health and/or the environment. Check the regulations in your workplace. Disposal of used filters and dust bags must be made in accordance with governmental regulations.

# Maintenance and Service

- Before carrying out any maintenance or service, the power supply must be removed from the wall socket. This does not apply for the manual cleaning of the filter.

- Check the filter regularly, at least once a week or other suitable interval depending on use. If necessary, clean the filter (see 8.4 Manual Cleaning of the Polyester Filter (Back flush))

- Change the filter at least once a year or more frequently depending on use. (See 8.2 Replacement of the Polyester Filter and 8.3 Replacement of the Hepa Filters )

- Change the filter if it shows any sign of damage or hole.

- Change the dust bag before it becomes too full. (See 8.1 Replacement of the Dust Bag)

- The mobile vacuum cleaner is not to be used for suction of water or any other liquid material. Should liquid enter the mobile vacuum cleaner, it must be taken apart and dried.

- Please note that service and repair of the electrical system is only to be done by authorised staff.

# Instructions for Maintenance

## Replacement of the Dust Bag

- Unplug the power supply from the wall socket.

- Loosen the strap securing the bag holder in place.

- Close the bag with the sealing strip which you can find at the upper edge of the dust bag.

- Remove the dust bag carefully to keep it from being damaged.

- Take a new bag and place its upper edge under the strap.

- Tighten the strap to secure the bag in place.

The dust bag might contain hazardous and poisonous dust and should therefore be disposed off according to governmental regulations. Used dust bags should always be closed completely and be treated carefully. Use only original dust bags.

Figure 2 Dust bag holder

## Replacement of the Polyester Filter

When replacing the filter, it is recommended to use a breathing mask. Always treat new and used filters with utmost care. Even a very small damage or hole on a filter will severely reduce the filtration. A used filter may contain dust, which is harmful to the health and/or the environment and should therefore be disposed of according to governmental regulations. Put the used filter in a large plastic bag and seal it carefully. Only use original filter.

- Unplug the power supply from the wall socket.

- Release the two toggle fasteners that hold the top cover in place (see figure 3).

- Lift off the top.

- Carefully lift out the filter housing with filter so that the dust does not spread out.

- Place the filter housing with filter upside down on the floor.

- Remove the nut and shim (M8, 13 mm wrench) located at the bottom of the filter.

- Put a plastic bag around filter and then remove the filter from the filter housing.

- Clean the housing and fit a new filter. Make sure that the filter is correctly centred in the filter housing. Fit the shim and nut. Tighten the nut so that the distance between the filter and the filter top is approximately 8 mm.

- Lift the filter back into the cyclone. Make sure that the gasket is in the right position.

- Mount the top cover on the cyclone.

- Tighten the two toggle fasteners.

Figure 3 Top cover (ME 2800)

## Replacement of the HEPA Filter(s)

When replacing the filter, it is recommended to use a breathing mask. Always treat new and used filters with utmost care. Even a very small damage or hole on a filter will severely reduce the filtration. A used filter may contain dust, which is harmful to the health and/or the environment and should therefore be disposed of according to governmental regulations. Put the used filter in a large plastic bag and seal it carefully. Only use original filter. Please note that the explanations are similar for the ME 1300 which possesses only one HEPA filter instead of two.

- Unplug the power supply from the wall socket.

- Unscrew the two black knobs (see figure 4).

- Lift off the tops of the HEPA filter housing carefully. The hose will allow you to do that without having to be removed.

- Put a plastic bag around the filters and then remove the filters from the filter tops.

- Fit new filters.

- Lift the filters back into the HEPA filter housing. Make sure that the filters are correctly centred in the filter housing and that the gasket is in the right position.

- Screw the two black knobs in order to secure the housings.

Figure 4 Top of the HEPA filter housings on a ME 2800

## Manual Cleaning of the Polyester Filter (Back flush)

(see figure 3)

Start the mobile vacuum cleaner by turning the switch to 2.

Place a hand at the end of the hose (alternatively on the pipe if the hose is removed, but the hose will provide better results).

Press the lever.

Repeat a few times for optimising the cleaning of the filter.

Turn off the unit by turning the switch to 0.

If the suction capacity is still low, this procedure may be repeated. If the suction capacity is still low after several back flushes, the filter must be replaced.

# Trouble-shooting

Must be carried out by an authorised professional!

- The mobile vacuum cleaner does not start, neither with main switch in 1st or 2nd position.

- Check that there is power to the vacuum cleaner.

- If any of above protector or fuse will go out again at a new attempt to start the machine, the probable cause is a shortcut. Before a new attempt, the electrical installation and power supply must be checked by an electrician for a possible shortcut.

- Poor suction.

- Clean or replace the filter. (See 8.2 Replacement of the Polyester Filter and 8.3 Replacement of the HEPA Filter(s)) If this does not help, the density of the piping system must be checked.

- Unusual noise from vacuum motor

- Turn off the unit immediately and contact the supplier.

- The dust bag is sucked up into the cyclone/filter housing.

- Check that the bottom valve is not obstructed and that it can fully close.

# EC DECLARATION OF CONFORMITY

Manufacturer:	Centraction AB

Industrivägen 7

433 61 Sävedalen

Sweden

Product designation:	Mobile Vacuum Cleaner, 
Type ME 1300, ME 2800

We declare that the above-mentioned products comply with the following European Directives:

- Low Voltage Directive 73/23/EEC with amendments,

- Machinery Directive 89/392/EEC with amendments,

- EMC Directive 89/336/EEC with regards to the Harmonised Standard EN 60 439-1

Sävedalen, 17 January 2010

Centraction AB

Björn Cagner

# Text boxes

1

6

2

5

3

4

Strap

Top cover

Lever for filter cleaning

Toggle fastener

Hoses

Knobs